## Slide 1
The Scientific Experiments Planned For The Rakia Mission
In partnership with the Davidson institute of science education the educational arm of the Weizmann institute

## Slide 2: FLUTE
Flute - fluidic telescope experiment: creating a lens using a viscous fluid in microgravity conditions for optical use

## Slide 3: Rakia Space Mission
The Ramon foundation and the Israel space agency are sending the second Israeli to space, Eytan Stibbe, on the Rakia mission to the international space station.
Eytan will be launched into space along with over 30 scientific experiments for him to conduct while there. The mission will enable Israeli entrepreneurs, scientists, and researchers to promote innovation.
Notes: The Ramon Foundation and the Israel Space Agency at the Ministry of Innovation, Science and Technology is sending the second Israeli to space, Eytan Stibbe, on a mission of great national and historic significance. The Rakia Mission is designed to inspire the younger generation and to boost and expand the Israeli space industry. In February 2022, a mission with a significant Israeli presence will set out to the International Space Station. This mission will be able to make a valuable contribution to the development of the space industry, and to improve life on Earth.
The International Space Station orbits the Earth at a fixed speed, 400 km above us, and like in space, there is microgravity on it.
The mission will enable Israeli entrepreneurs, scientists, and researchers to promote innovative ideas and provide them with a rare opportunity to test their initiatives in a unique research environment, thereby contributing to the Israeli and international space industry and research. The mission will also make a range of educational activities accessible to all children in Israel. This will be the first ever opportunity for Israeli children and youth to access the International Space Station – in Hebrew.
Approx. 40 scientific experiments to be conducted in space will be launched together with the astronauts
The Rakia Mission will enable Israel entrepreneurs, scientists, and researchers to promote innovative ideas and to test their initiatives in a unique research environment. By doing so, it will contribute to promoting Israeli and international research.
The experiments to be launched into space were carefully selected and span a variety of fields including biology, human physiology, agriculture, and more.

## Slide 4
Fluidic telescope experiment: creating a lens using a viscous fluid in microgravity conditions for optical uses.
XX
    The fluidic telescope experiment is a joint project between the Technion's faculty of mechanical engineering and Nasa. Its goal is to enable the fabrication of optical components in space for the first time ever, using the physics of fluids in microgravity.
To watch the video
where Prof. Moran Bercovici explains about the experiment
The researcher of the experiment:
Prof. Moran Bercovici
Notes: https://www.youtube.com/watch?v=kcGVK9K1530

## Slide 5: Flute - Fluidic Telescope Experiment Innovation In Space
The experiment aims to demonstrate how fluids can be formed into the required shapes for optical components without the need for complex mechanical processes, in a way that is simpler, quicker, and at a higher quality than on earth.
The project’s success will revolutionize the industry of manufacturing in space, and also in the field of astronomy, and will pave the way for the construction of space telescopes with diameters reaching dozens of meters.

## Slide 6: Flute - Fluidic Telescope Experiment
Innovation on earth
On earth, the experiment will lead to a revolution: significantly reducing the complexity and time it takes to manufacture lenses for optical products such as eyeglasses and camera lenses.
When the manufacturing process is made simple and at exceptional quality, it will also reduce the cost: this will make eyeglasses more ready accessible in poorer parts of the world.

## Slide 7: FLUIDIC TELESCOPE EXPERIMENT
What The Experiment Looks Like On Earth
The lenses are made of a liquid polymer. The researchers inject the polymer into a ring Placed inside a container filled with a solution of water and glycerin. The amount of glycerin in the water is planned so that the density of the solution is completely identical to the density of the polymer, so it floats within the fluid. The polymer sticks to the inside of the ring and remains attached to it. Because the polymer and the solution are insoluble with each other, a smooth contact surface is created between the two liquids, which is controlled by the surface tension.
Notes: The lenses are made of polymer – a liquid material built of large molecules that stimulates a rapid chemical process that causes the molecules to bond with each other when exposed to ultraviolet (UV) radiation, with the liquid becoming a solid.
The researchers inject the polymer into a ring placed inside a container filled with a solution of water and glycerin. The amount of glycerin in the water is planned so that the density of the solution is completely identical to the density of the polymer. This achieves neutral buoyancy – The polymer neither sinks to the bottom nor floats to the surface of the water.
The polymer likes to adhere to the inside of the ring and remains attached to it. Because the polymer and the solution are insoluble with each other (they don’t mix, like oil and water), a smooth contact surface is created between the two liquids, which is controlled by the surface tension. This creates the shape of a perfect lens!

## Slide 8
Notes: https://www.youtube.com/watch?app=desktop&v=https://www.youtube.com/watch?app=desktop&v=p8FAy4q6vjQ&feature=youtu.be
&feature=youtu.be

## Slide 9: FLUIDIC TELESCOPE EXPERIMENT
  What The Experiment Looks Like On Earth
  This creates the shape of a perfect lens!
  The process by which the polymer solidifies is called polymerization, and in this case it occurs by exposure to uv radiation.
Notes: The lenses are made of polymer – a liquid material built of large molecules that stimulates a rapid chemical process that causes the molecules to bond with each other when exposed to ultraviolet (UV) radiation, with the liquid becoming a solid.
The researchers inject the polymer into a ring placed inside a container filled with a solution of water and glycerin. The amount of glycerin in the water is planned so that the density of the solution is completely identical to the density of the polymer. This achieves neutral buoyancy – The polymer neither sinks to the bottom nor floats to the surface of the water.
The polymer likes to adhere to the inside of the ring and remains attached to it. Because the polymer and the solution are insoluble with each other (they don’t mix, like oil and water), a smooth contact surface is created between the two liquids, which is controlled by the surface tension. This creates the shape of a perfect lens!

## Slide 11
Notes: The solution in the experiment on Earth enables neutral buoyancy and resembles microgravity conditions. In the experiment in space, the solution will be unnecessary and the lens is expected to “float” in the air, just like in water.
And yet...we don’t know for certain. The experiment in space is supposed to prove the expected hypothesis.
What might be different?
Tremors can disrupt the lens’ shape. When there is a buoyancy fluid surrounding the lens, it acts to restrain (or reduce) and rapidly suppresses disturbances. Without the buoyancy fluid, disturbances may manifest more significantly on the surface.

## Slide 12: A Stand That Stabilizes The Ring Into Which The Lens Is Poured
    On earth, weights are attached to the stand stabilizing the lens’s frame, and they prevent it from floating in the solution. Weights won’t help to stabilize the stand in space.
    In space, things are stabilized mostly using hook and loop fasteners (such as Velcro), magnets (like fridge magnets), or rubber bands, which allow for strong fastening and release even in microgravity conditions.

## Slide 13: The Need To Solidify The Lens Using UV Radiation
In microgravity, the lens can also be useful even without solidification.
In this form, it is possible to create a folding space telescope with liquid lenses, for example.
A polymer is a macromolecule made up of many parts (from the Greek "Polys" = many and "Meros" = parts). These parts are similar units that are linked in chains containing thousands of units. The process whereby these units join to create a polymer is called a “polymerization reaction”.
To bring the lens to earth, it will need to undergo polymerization and solidification using UV radiation.

## Slide 14: Air Bubbles Trapped In The Lens
Air bubbles that get accidentally trapped in the liquid damage the quality of the lens. On earth, the air density is significantly lower than that of the liquid, and therefore on earth, the air bubbles float to the top of the container.
When there is no gravity, there is also no buoyancy. Bubbles that are trapped in the liquid will stay where they are. We must therefore be very careful not to accidentally introduce air bubbles during the lens creation process.

## Slide 15: Safety Of Liquids
The solution and the polymer are packaged in hermetically sealed bottles, both on earth and in space. On earth, if we “missed” during the injection process, the polymer drop would fall onto the table and we could wipe it up with a cloth.
Without gravity, the polymer drops will float around the space station. On the international space lab, all liquids require double packaging. The current experiment will be triple packaged.
Notes: On the international space lab, all liquids require double packaging. The current experiment will be triple packaged: The lens polymer will be in a bottle, the bottle in a sealed bag, and the entire experiment will be performed inside a closed and transparent flexible box that allows the person performing it to insert their hands and conduct the experiment without the risk of liquids or gases escaping into the space station.
On Earth, if we “missed” during the injection process, the polymer drop would fall on the table and we could wipe it up with a cloth. Without gravity, the polymer drops will float around and it may be challenging to catch them and prevent them from reaching other sensitive equipment.
Polymers sometimes carry an unpleasant odor (like glue). On Earth it’s possible to open a window and air out the room, but on a space station you can’t open any windows! It’s imperative to ensure that all the materials sent into space are neither hazardous nor smelly.

## Slide 16: Safety Of Gases
On a space station you can’t open any windows!
It’s imperative to ensure that all the materials sent into space are neither hazardous nor smelly.
Polymers sometimes have an unpleasant odor (like glue). On earth it’s possible to open a window and air out the room.
Notes: NASA conducted comprehensive tests on the polymer making up the lens, to ensure that there are no toxic and volatile substances during the lens formation process.

## Slide 17: Closing Boxes
The general structure of the experiment system resembles the one on earth – the frame into which the polymer is injected, which is closed with a lid that contains the ultraviolet light to stimulate the polymerization process.
On earth, the lid remains closed because of its weight, and doesn’t need to be locked.
But in space, there is no force that will hold the lid over the box if it’s just placed on top.
Therefore, it’s important that each lid is fastened with hook and loop fasteners (Velcro) to keep it firmly in place.

## Slide 18
Before launching into space, Nasa allowed the entire lab team to try and create the lens in a zero-g flight.
This is a special flight where the plane simulates a free fall for 20 seconds and accordingly simulates the same microgravity conditions on the international space station.
Notes: https://www.youtube.com/watch?v=XE1wlo7IJrU&feature=youtu.be

## Slide 19
Eytan Stibbe will perform the fluidic telescope experiment during the mission week at the end of march 2022
The experiment will be broadcast through the website.
Make sure to watch the broadcast!
/HTTPS://WWW.RAKIAMISSION.CO.IL
Notes: https://www.eng.rakiamission.co.il/